## Slide 1
Summer water temperature for 13 continuous monitoring locations in the Brodhead Watershed
Prepared by David Bressler (Stroud Water Research Center) for Brodhead Watershed Association
Support from John Jackson (Stroud Water Research Center) and Keith Fritschie (NJ Trout Unlimited Volunteer)
Notes: 1

## Slide 2: Map of 12 EnviroDIY stations and 1 USGS station
Upper McMichaels
Creek (BWA9)
McMichaels Creek on Pomeroy (BWA7)
Pocono Creek on Rail Gap (BWA6)
Marshalls Creek Falls (BWA10)
Pocono Creek on Tannersville Woods (BWA8)
Paradise Creek above Brodhead (PKPC3S)
Brodhead Creek above Paradise (PKBH7S)
Butz Run (BWA4)
Forest Hills Run (BWA1)
Swiftwater Creek (Swift 314)
Yankee Run (BWA Logger 5)
Lower Mill Creek (BWA3)
USGS, Brodhead Creek near Analomink (01440400)

## Slide 3: Average Summer Water Temperature (60-day, July-Aug) – Coarse Trout Thresholds
Red >21 C°(70 F°) = Non-Sustaining
Yellow 19-21 C° (66-70 F°) = Stressful
Green <19 C° (66 F°) = Supportive
https://stock.adobe.com/images/traffic-light-red-yellow-green-lights-go-wait-or-slow-stop-international-traffic-light-s-day-applique-vector-design-illustrations/211926764
USGS SHEDS Brook trout model, NV DEP 2017, Chadwick et al. 2015, Kratzer 2013, Wehrly et al 2007; personal communication Keith Fritschie (VA DEC); PA DEP Ch 93 Water Quality Standards

## Slide 4: Average Summer Water Temperature for 13 locations in Brodhead watershed (Year 2023)
Average Summer Water Temperature (C°)
Non-Sustaining, >21 C°(70 F°)
Stressful, 19-21 C° (66-70 F°)
Supportive, <19 C° (66 F°)

## Slide 5: Yankee Run (BWA Logger 5)
Average Summer Water Temperature = 13.2 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
*Note – spikes represent warm storm water runoff, which can be stressful to trout, especially larger fish
Water Temperature (C°)
Date, year 2023

## Slide 6: Swiftwater Creek (Swift 314)
Average Summer Water Temperature = 14.7 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Data error - disregard
Data error - disregard
Water Temperature (C°)
Date, year 2023

## Slide 7: Lower Mill Creek (BWA3)
Average Summer Water Temperature = 16.6 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Water Temperature (C°)
Date, year 2023

## Slide 8: Upper McMichaels Creek (BWA9)
Average Summer Water Temperature = 16.8 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Water Temperature (C°)
Date, year 2023
*Note – incomplete data set (July was hotter so summer average may be >16.8 C°)

## Slide 9: Pocono Creek at Tannersville Woods (BWA8)
Average Summer Water Temperature = 18.4 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Water Temperature (C°)
Date, year 2023
*Note – incomplete data set (July was hotter so summer average may be >18.4 C°)

## Slide 10: Marshalls Creek Falls (BWA10)
*Average Summer Water Temperature = 18.7 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
*Note – incomplete data set (July was hotter so summer average may be >18.7 C°)
Water Temperature (C°)
Date, year 2023
Data error - disregard

## Slide 11: Paradise Creek above Brodhead (PKPC3S)
Average Summer Water Temperature = 19.4 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Water Temperature (C°)
Date, year 2023
*Note – incomplete data set (July was hotter so summer average may be >19.4 C°)

## Slide 12: Butz Run (BWA4)
Average Summer Water Temperature = 19.4 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Water Temperature (C°)
Date, year 2023
Data error - disregard
Data error - disregard

## Slide 13: Brodhead Creek above Paradise (PKBH7S)
Average Summer Water Temperature = 19.7 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Data error - disregard
Data error - disregard
Water Temperature (C°)
Date, year 2023

## Slide 14: Pocono Creek at Rail Gap (BWA6)
Average Summer Water Temperature = 19.8 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Water Temperature (C°)
Date, year 2023
Data error - disregard

## Slide 15: McMichaels Creek on Pomeroy (BWA7)
Average Summer Water Temperature = 19.8 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Water Temperature (C°)
Date, year 2023
*Note – incomplete data set (July was hotter so summer average may be >19.8 C°)

## Slide 16: Forest Hills Run (BWA1)
Average Summer Water Temperature = 20.7 C°
PA DEP Maximum Stream Temperature for Cold Water Fish (66 F°, 19 C°)
Water Temperature (C°)
Date, year 2023